## Slide 1
STUDENTS PROFESSOR
Catapano Serena Fabio Ruggiero
Varone Emanuela
Autonomous Bicycle Parking
Autonomous Bicycle Parking- Final discussion
01/22
Final Project:

## Slide 2
02/22
comparison of four different controllers to identify the optimal solution
  Technical challenge:
Autonomous Bicycle Parking- Final discussion
Why Autonomous Parking?
  Primary objective:
  Approach:
simultaneously coordinate route planning, vehicle control and kinematic constraint management
develop, implement and critically analyse a complete autonomous parking bicycle

## Slide 3
MAP
PRE-PROCESSING
PATH PLANNING WITH RRT*
POST-PROCESSING
TRAJECTORY
Implementation Workflow
03/22
Autonomous Bicycle Parking- Final discussion
Resolution: 0.1m per cell
Inflation radius: 0.5m for safety
Minimum Turning Radius: 4
Connection Distance : 30
Goal Tolerance: [0.5, 0.5, 10]
Minimum Iterations: 2000

## Slide 4
Bicycle Models : Two Modeling Approaches
Kinematic Model
Controllers: Pure Pursuit, MPC, Hybrid
Key Features:
  Pure rolling, no slippage
  Low speed
  Geometric relations of vehicle movement only
  Completely ignoring the physical forces involved
  Simplicity of implementation
04/22
Autonomous Bicycle Parking- Final discussion
Dynamic Model
Controller: Stanley Controller
Key Features:
  Includes lateral forces and tire dynamics
  Valid at all speeds
  Higher computational complexity
  Captures real behaviour (drift, skidding)

## Slide 5
Key Features:
05/22
Autonomous Bicycle Parking- Final discussion
Pure Pursuit Controller
  Geometry: triangle between current position, look-ahead point and centre of rotation
  Key formula: δ = atan( 2L × sin(α) / ld )
  Innovation: Multi-stage adaptive look-ahead distance
Operating phases:
  Start (0-5s): the controller applies a conservative strategy to ensure a smooth and safe start
  Cruise (>3m from target): the look-ahead distance varies dynamically (2-15m)
  Approach (<3m): control accuracy gradually increased (responsiveness improved and faster corrections)
  Final accuracy (<0.3m): maximum precision mode (control gain tripled for aggressive corrections)

## Slide 6
Results:
06/22
Autonomous Bicycle Parking- Final discussion
  Good average tracking performance (maximum position error and RMS)
  Excellent convergence to the desired parking configuration (minimal final errors)
  Frequently demands high control efforts (saturation of 3.10%)

## Slide 7
07/22
Autonomous Bicycle Parking- Final discussion

## Slide 8
Model Predictive Control
Strategy: "Look Ahead and Optimize"
TRANSFORMATION INTO ERROR COORDINATES
QUADRATIC COST FUNCTION
QUADRATIC PROGRAMMING SOLVER
08/22
Autonomous Bicycle Parking- Final discussion
  Linearization
  Discretization
  Multi-Step Predictive Model
Control Input Constraints

## Slide 9
Parameter Tuning
09/22
Autonomous Bicycle Parking- Final discussion
Q Weights Optimization (State Error Penalties)
  Q₁/Q₂ = 10 ensures lateral error priority over longitudinal
  Q₃/Q₂ = 2 balances heading alignment with timing flexibility

## Slide 10
Parameter Tuning
10/22
Autonomous Bicycle Parking- Final discussion
R Weights & Prediction Horizon
Adaptive Weight Strategy
  if approaching_target:
  Q_adaptive(1) = Q_nominal(1) * 2.0 // Double lateral importance
  Q_adaptive(3) = Q_nominal(3) * 1.5 // Increase heading alignment
  R_adaptive(2) = R_nominal(2) * 2.0 // Penalize steering variations
Final choice: Nₚ = 6 provides 0.6s anticipation with 8ms computation time

## Slide 11
11/22
Autonomous Bicycle Parking- Final discussion
Results:
  Mixed performance profile
  Never reaches actuator limits and maintains smooth control throughout the maneuver (saturation at 0.00%)
  Fails to converge to the desired parking position accurately (final position error)
  Orientation control is more effectively managed than position tracking

## Slide 12
12/22
Autonomous Bicycle Parking- Final discussion

## Slide 13
ERROR PREPROCESSING MODULE
OPERATIONAL DECISION MODULE
APPROACHING TARGET
PARKING COMPLETED
13/22
Autonomous Bicycle Parking- Final discussion
Hybrid Multi-Mode Controller
  Feedforward-feedback control for longitudinal tracking
  Stanley-type lateral control for transverse error correction
  Heading control for orientation correction
  Supervisory logic for managing the different operating phases
Modular Architecture
Integrated components:
  v_cmd = v_base × lateral_factor × heading_factor (v_base = v_ref + k₁·e_long)
  φ_lateral = atan2(k_stanley·e_lat, max(0.5, |v_cmd|))
  φ_cmd = φ_feedforward + φ_lateral + φ_heading
φ_heading = -k₂·e_θ
φ_feedforward = atan(L·θ̇d/v_cmd)

## Slide 14
14/22
Autonomous Bicycle Parking- Final discussion
Results:
  Excels at maintaining close adherence to the reference trajectory
  Not only tracks the position accurately, but also ensures proper orientation alignment
  Occasionally demands control inputs at or near the actuator limits (1.60% saturation)

## Slide 15
15/22
Autonomous Bicycle Parking- Final discussion

## Slide 16
STANLEY LONGITUDINAL CONTROLLER
STANLEY LATERAL CONTROLLER
16/22
Autonomous Bicycle Parking- Final discussion
Stanley Controller
HANDLES MOVEMENT ALONG THE DIRECTION
OF VEHICLE TRAVE
HANDLES MOVEMENT PERPENDICULAR
TO THE DIRECTION OF TRAVEL
The algorithm combines two intuitive actions: first, orient the vehicle towards the target point to correct the orientation
error, then add an additional correction proportional to the lateral distance from the target point to ensure stable
convergence. The Stanley control law can be expressed mathematically as:

## Slide 17
17/22
Autonomous Bicycle Parking- Final discussion
Results:
  Achieves perfect control feasibility with 0.00% saturation
  Operation strategy: it allows larger transient errors but maintains smooth, feasible control throughout the maneuver. The front-wheel position feedback mechanism characteristic of Stanley control appears to provide natural damping that prevents excessive control demands.

## Slide 18
18/22
Autonomous Bicycle Parking- Final discussion

## Slide 19
19/22
Autonomous Bicycle Parking- Final discussion
Comparative analysis - TRACKING
  Hybrid dominates overall tracking performance
  Pure Pursuit excels in final convergence precision
  MPC sacrifices accuracy for control smoothness
  Stanley unsuitable for tight nonholonomic constraints
Data clearly demonstrates the hybrid approach superiority in balancing tracking precision with final convergence accuracy

## Slide 20
20/22
Autonomous Bicycle Parking- Final discussion
Comparative analysis - CONTROL
  Saturation vs Control: MPC achieves zero saturation with optimal feasibility
  Efficiency vs Aggressiveness: Pure Pursuit shows moderate saturation but remains acceptable
  Balance vs Performance: Hybrid maintains low saturation while managing complexity
Actuator saturation is a critical indicator of practical feasibility. Both MPC and Stanley achieve zero saturation with optimal control demands, while Hybrid maintains excellent performance with minimal saturation at 1.60%. Pure Pursuit shows higher saturation at 3.10% but remains within acceptable operational limits.

## Slide 21
  Experimental validation on real vehicle
  Robustness to uncertainties and disturbances
  Computational optimisation for real-time
  Extension to parallel and oblique car parks
21/22
Autonomous Bicycle Parking- Final discussion
FUTURE DEVELOPMENTS

## Slide 22
22/22
Autonomous Bicycle Parking- Final discussion
THANKS FOR THE ATTENTION